## Slide 1: ESP8266 Node MCU
Introduction
Pinout
Working

## Slide 2: Why ESP8266??
Other methods to connect to wifi:
1) Arduino(Microcontroller) + Wifi-Sheild (Rs. 4500)
2) CC3000 Wi-fi( Rs. 2400)
3) ESP8266 ( Rs. 250-400)
4) ESP8266 Node MCU ( Rs. 300-400)

## Slide 3: ESP8266
The ESP8266 is a low cost Wifi chip from Espressif, that you can use with your Arduino (for example) or even use it in standalone
This small module allows micro-controllers to connect to a Wi-Fi network and make simple TCP/IP connections.

## Slide 4: What is Node MCU?
The NodeMCU is the name of a micro controller designed by Espressif Systems. The ESP8266 itself is a self-contained Wi-Fi networking solution offering as a bridge from existing micro controller to Wi-Fi and is also capable of running self-contained applications.
This module comes with a built in USB connector and a rich assortment of pin-outs.
With a micro USB cable, you can connect NodeMCU devkit to your laptop and flash it without any trouble, just like Arduino. It is also immediately breadboard friendly.

## Slide 6
An open-source firmware and development kit that helps you to prototype your IOT product.
Simple ESP8266 can only be used to connect other micro-controllers like Arduino to internet with its inbuilt wi-fi chip. But with Node MCU development kit this hardware module can use its GPIO pins to connect to other peripherals without help of any other micro-controller.
That means you can program NodeMCU to work with other devices using GPIO along with connected wi-fi.
This make NodeMCU ideal for use in Iot projects. These can be programmed and then connected with other hardware like relays, buttons etc via GPIO and also to wi-fi. Over wi-fi they can contact with some more powerful machines like RaspberryPi using protocols like MQTT.
Using wi-fi these nodes can transfer states to main machine located on network or some sort of server. Server/Main machine can also issue commands to these nodes which they can perform as per their programming.

## Slide 7: Specification:
• Voltage: 3.3V.
• Wi-Fi Direct (P2P), soft-AP.
• Current consumption: 10uA~170mA.
• Flash memory : 4MB, total attachable 16MB max (512K normal).
• Integrated TCP/IP protocol stack.
• Processor: Tensilica L106 32-bit.
• Processor speed: 80~160MHz.
• RAM: 32K + 80K.
• GPIOs: 17 (multiplexed with other functions).
• Analog to Digital: 1 input with 1024 step resolution.
• +19.5dBm output power in 802.11b mode
• 802.11 support: b/g/n.
• Maximum concurrent TCP connections: 5.

## Slide 9: Node MCU Hardware:
ESP8266 : It is main chip which with inbuilt w-ifi
USB to UART convertor : This chip will convert USB data to UART(Universal Asynchronous Receiver-Transmitter) data which main chip can understand
Voltage regulators: Converts input voltage to 3.3V.
Status LED : This LED is basically used to show current status like flashing/booting
MicroUSB port : Connect board to Computer for programming and powering the board.
Reset/Flash buttons : Perform actions on board.
GPIO pins : To connect board with other peripherals.

## Slide 11: Pin Definition

## Slide 12: Using Node MCU with PC
1) Install Arduino IDE.
2) Edit board manager URL for specific board.
  a) File -> Preferences -> URL for additional board.
3) Install Board Library in Arduino IDE:
  a) Tools -> Board -> Boards Manager -> Install ESP8266 boards.
4) Install Driver for USB Cable:
  a) Device Manager -> USB Port
5) Select the required board and COM port.
  a) Board: NodeMCU 1.0(ESP-12E Module)
  b) Port: Select the available COM