## Slide 1: 2) Doorbell security light
Be secure always.

## Slide 2
introduction
INSPIRATION:
Many people live alone and at lonely locations across the city.
During night, if someone rings the doorbell, the person cannot see who is it outside.
This system will help them recognize the person and see if any threat is present.
AIM:
Whenever at night, doorbell is pressed the bulb outside glows for some time and helps the owner see the person outside and can reset the circuit to turn off the bulb. The bulb automatically gets off after a certain time if the owner doesn’t respond and saves electricity.

## Slide 3: Block Diagram
Bell Switch
Light Sensing Circuit
Timer
Circuit
Bulb
Triggering Circuit
Doorbell

## Slide 4
Concept and working
When bell switch is pressed during the night, not only the bell rings but the bulb connected to it also glows.
In order to turn the bulb off, a reset pushbutton is provided.
Supply is fed to the collector of transistor BC547.
A LDR is connected to the base of this transistor.
When bell switch is closed, the bell rings.
Monostable timer turns on the bulb through a relay.

## Slide 5
Components
1) 7805 : Voltage Regulator
2) LDR
3) Potentiometer
4) BC547
5) Capacitor and Resistors
6) 555 Timer
7) Silicon Diode : 1N4001
8) 7404 : NOT logic gate
9) Screw terminal connector

## Slide 6
Related documents
Schematic:
2) DSL\DSL_Schematic
PCB Layout:
2) DSL\DSL_PCB
Datasheets:
2) DSL\DSL_Datasheets

## Slide 7
calculations
LDR Resistance Limits Used:
DARK: 50 kΩ
LIGHT: 1 kΩ
555 Timer Monostable Mode:
T = 1.1 * R * C
For T = 1.5 mins, C = 1000uF and R= 100 k Ω

## Slide 8: Limitations
1) LDR is very sensitive and should be present at a specific place.
2) Only useful in certain conditions.

## Slide 9: advantages
Low cost.
Automatic Switch-off.