## Slide 1: 3) Fire alarm
Be secure always.

## Slide 2: introduction
INSPIRATION:
  Most fire alarm circuits are microcontroller based, thus costly.
  Only a single sensor to detect fire so work in certain conditions only.
  A multi-sensor alarm without microcontroller.
  Reliable and cheap.
AIM:
  To build a fire alarm which detects high temperature, smoke and fire flames and sounds an alarm if either of the three conditions are present. The sensitivity of the sensor should be adjustable for it to be installed in various places like home, factory, etc.

## Slide 3: Block Diagram
Flame Sensor
Temperature Sensor
Smoke Sensor
Comparator
Alarm

## Slide 4: Concept and working
On detection of either flames or high temperatures or smoke, alarm is raised.
Dual comparator LM358 triggers npn transistor.
Transistor conducts and energizes relay to activate the alarm connected across it.
Adjustable temperature and smoke threshold values.
Safety indicator led is present.
Circuit functional led is present.

## Slide 5: Components
MQ 135
IR Flame sensor
LM35
LM358
Relay
Led
Resistors
Pinhead PCB Connectors

## Slide 6: Related documents
Schematic:
3) Fire Alarm\FA_Schematic
Simulation:
3) Fire Alarm\FA_Simulation
PCB Layout:
3) Fire Alarm\FA_Simulation
Datasheets:
3) Fire Alarm\FA_Datasheets

## Slide 7: calculations
Vref:
1) LM35: 0.45 v ( 45
2) Flame sensor : 4 V ( Active Low Sensor)
3) MQ135: 3.5V (By practical testing)

## Slide 8: Limitations
1) Flame sensor’s sensing distance depends on the intensity of the flame.
2) LM35 takes some time to heat up.
3) MQ135 has 48 hours preheat time.

## Slide 9: advantages
1) All sensors can be configured for different environments.
2) Cheaper than current available systems.