## Slide 1: 4) Person counter
Be secure always.

## Slide 2
introduction
INSPIRATION:
Firemen face a serious issue:
They do not know the exact number of people inside a burning building.
This lack of information is harmful to them as well as others.
It would make their jobs easier they knew the exact number of people inside.
AIM:
Our aim is to build a reliable and accurate counter which can count the total strength currently present in a particular enclosed area.

## Slide 3
Concept and working
One laser is outside, one inside the door and is focused on LDR.
As a person passes, laser is cut.
Signal from the LDR circuit is given to the main circuit.
Depending on the signal flow, count is either increased or decreased.
Thus if person comes in, count is increased.
If person goes out, count is decresed.

## Slide 4: Components
1) Counter IC: 74193
2) 7 Segment LED Display
3) LED Driver IC: 4511
4) 74xx Logic Gates
5) Laser
6) LDR
7) NPN Transistor BC547
8) D flipflop : 7474

## Slide 5
Related documents
Schematic:
4) Person Counter\PC_Schematic
Simulation:
4) Person Counter\PC_Simulation
PCB Layout:
4) Person Counter\PC_PCb
Datasheets:
4) Person Counter\PC_Datasheets

## Slide 6: calculations
When Laser ON:
Rldr = 400 Ω
So, Vb > 0.8 V
Therefore, R > 80 Ω
When Laser OFF:
Rldr = 25 KΩ
So, Vb < 0.6 V
Therefore, R < 3.5 KΩ

## Slide 7: Limitations of circuit
Limitations in speed of sensing of the module.
LDR are very sensitive to light, and may malfunction in extreme cases.